## Slide 1: ERTMS Solutions ERTMSFormalSpecs (EFS) A domain specific language to formalize ERTMS specifications for onboard unit development
  Stanislas Pinte
  Laurent Ferier
  Svitlana Lukicheva

## Slide 2: The Context
Hardware
Supplier dependant
ERTMS business logic
Fully defined by Subset-026
Safety software architecture
Supplier dependant

## Slide 3: The Challenge
Subset-026
  Specification of the EVC behaviour
    Normative document
  Issues
    Natural language
    Structure
    Size
    Completeness
    Consistency
    Releases

## Slide 4: Impact for the supplier and user
Interpretation issues
  Interoperability
  Safety
Costs
  Development costs
  Maintenance costs

## Slide 5: ERTMSFormalSpecs
Ada
C
B
100% ERTMS Business Logic
Formal Language
ERTMS Specifications
CASE tool
Target
SIL4
Interpreter
Test tools

## Slide 6: Encompasses the complete process
Requirements / Model / Testing
Traceability
  Model & functional tests
  Subset-026
  New requirements: gaps in Subset-026
Metrics
Review
History

## Slide 7: Understandability
Model as close as possible to Subset-026
  Formal language should match Subset-026 expressivity
  High level artifacts
    State machines
    Interaction diagrams
    Braking curves

## Slide 8: Testing
100% model in the loop testing
  Functional tests, related to Subset-026 requirements
  Integration tests as expressed in Subset-076
Niceties
  Model animation
  Test traces
  Step by step folding / unfolding

## Slide 9: Interpretation model
EFS Model
Input
Output
Internal
Input
Input
Input
Output
Output
Output
Validation +
Business
Business
Cleanup
Cleanup
Cleanup

## Slide 10: Interpretation model
Interpretation machine
  Based on variables (representing EVC state, input messages, …)
  Rule machine: for each rule
    Evaluate rule’s preconditions based on the variable’s state…
    … and if they are satisfied, apply rule’s body to change the interpretation machine’s internal variables
  One interpretation model:
    High level structures (state diagrams, tables) are translated into rules, and interpreted as such

## Slide 11
ERTMSFormalSpecs live presentation
The basics

## Slide 12: EFS DSL coverage
Typical data structures, used to describe
  internal data used to model concepts of chapter 2 and 3
  packets of chapter 7, messages from chapter 8
  functions, also used to model tables
State machines, used to describe
  mode transitions from chapter 4
  procedures of chapter 5
Rule based interpretation machine
  to model system behaviour (all chapters)
Braking curves
  Huge amount of chapter 3
Chapter 1
Chapter 2
Chapter 3
Chapter 4
Chapter 5
Chapter 6
Chapter 7
Chapter 8
Ch.3
Brake

## Slide 13: Braking curves

## Slide 14: Braking curves modeling
FUNCTION SpeedRestrictions(
Distance : Default.BaseTypes.Distance
) RETURNS Default.BaseTypes.Speed
// Value
=>
(REDUCE TSRs USING
MIN(
First => TSRSpeedRestriction(X, d),
Second => RESULT)
INITIAL_VALUE MaxSpeedFunction
)(Distance)
Model by functional composition
  Speed restriction example: TSRs
    Single TSR
    Several TSRs
  Handle other speed restrictions
    Provides a complex speed profile
    Explanation is available
FUNCTION TSRSpeedRestriction(
aTSR : TemporarySpeedRestriction
Distance : Default.BaseTypes.Distance
) RETURNS Default.BaseTypes.Speed
// During TSR
aTSR.Location <= Distance AND
Distance < aTSR.Location + TSRLength (aTSR)
=> aTSR.Speed
// Outside TSR
=> BaseTypes.Speed.MaxSpeed

## Slide 15: Deceleration factors
The same technique is applied to compute deceleration factors
Computation of the deceleration curves
  based on P (variant SBI, EBI)
  and the deceleration factor

## Slide 16: Braking curves

## Slide 17: Braking curves comparative results
Comparison with ERA braking curve spreadsheet
  Tool differences
    ERA spreadsheet handle a single target
    whereas EFS handles complex speed profiles
  Results
    Same results for the simplest cases (modulo ɛ)
    Similar results for complex deceleration factors
      due to discrete computation in the spreadsheet
      acceptable : initial train speed=140km/h induced Δ=20cm
      note : acceptable error not defined in Subset26

## Slide 18
ERTMSFormalSpecs live presentation
Braking curves

## Slide 19: Subset 076 - Scope
Subset 076
  Define interoperability tests between trackside & trainborne
    Inputs from either trackside or driver
    Expected output from EVC
  Define EVC integration tests
  Available as word documents, generated from an Access database
  The idea is to apply Subset-076 tests to EFS model.

## Slide 20: Subset-076 and EFS
S76 Access
databases
Textual import
EFS tests
database
Text
Model
Textual
tranlations
Integration model
  Source is the (non formal) subset 076 Access database
  Imported as structured text in the EFS test database
  Access databases are no more useful
  Automate the translation process
  Some parts might not be automated

## Slide 21: Translations
Subset-076 steps are expressed as plain English
Need to formalize this as
  Actions : changes in the system
  Expectations : expected system state
Translation dictionary
  Associate one (or more) English phrase with sequences of actions / expectations
The same translations rules can be applied to several Subset-076 test cases

## Slide 22
ERTMSFormalSpecs live presentation
Subset-076 integration

## Slide 23: Current status
Modeling status
  Subset-026: 3225 applicable requirements
  Modeled: 1061
  Completion: about 33 %
Testing
  Unit tests: 15% tested
  Subset-076:
    Database imporation tool complete
    Manual translation ongoing

## Slide 24: Your comments (questions, remarks, jokes) …
… are welcome!